## Slide 1
transit scheduling
Factors that go into bus and rail schedule design
Jolando Crane – Manager of Scheduling
Mark McComb – Rail Scheduler (Ctr)
12/6/2023

## Slide 2: Basics of transit scheduling
Consists of two elements
  How long it takes to get from one end to the other
  Time to recover at the end of the line

## Slide 3: How long to get from one end to the other
Factors that affect scheduled time
  Traffic
  Number of stops that are made
  Number of passengers boarding
  Countless other things (construction, traffic signals, development, etc.)
How long it takes varies throughout the day
  We group this into bands of time (such as AM peak, midday, or late night)
  Averages are used to determine the time that is used
  Recovery is a function of how long it takes

## Slide 4: Time to recover at the end of the line
Also known as layover time
Allows time to recover from delays
Allows the operator time to stretch and/or use the restroom

## Slide 5: Pulling it all together
When you add together the travel time and the recovery time in both directions then you can begin to schedule the service
  A bus route is like a racetrack, buses do laps (round trips)
  How long it takes to do a lap is the basis of all scheduling
  Then planning lets us know how often service should run
  Finally, we figure out how many buses are needed to run service at the desired frequency and create the schedules
Other factors we consider in schedule design

## Slide 6
Headway
Time between buses

## Slide 7
Headway
Time between buses

## Slide 8
Headway
Time between buses

## Slide 9
Headway
Time between buses
10
MIN

## Slide 10
Cycle Time = 60
# of Buses = 1
Headway = 60

## Slide 11
Cycle Time = 60
# of Buses = 2
Headway = 30

## Slide 12
Cycle Time = 60
# of Buses = 3
Headway = 20

## Slide 13
Cycle Time = 60
# of Buses = 4
Headway = 15

## Slide 14: Rail scheduling
At its core, rail scheduling is very similar to bus scheduling
Need to know how long it takes and how much recovery time is needed
Need to figure out how many trains are needed to provide frequency
But it is also different
There is only so much space at the end of the line to stage trains
The travel time is usually consistent throughout the day
Construction means single-tracking
Any change may affect multiple schedules
Most of the scheduling relates to construction and special events

## Slide 15: Example – Indian Creek Station Redesign
Construction will close off one of the two tracks
  Need to reschedule trains so there won’t be two trains at once
Other end of the line (H.E. Holmes) also is preferred to have one train at a time
Schedule will need to be shifted to line up trains on each end
  Also will need to shift Green line
  Also will need to adjust 5-8 other single tracking and special event schedules

## Slide 17: Indian Creek Station
Station will remain open
Island platform, normally train can be accessed from either side
Normally if a train is already at the station, an approaching train can cross and use the other side

## Slide 18: Indian Creek Station
Station will remain open
Island platform, normally train can be accessed from either side
Normally if a train is already at the station, an approaching train can cross and use the other side
With construction only one side (L or R) of the platform will be available
Now, if a train is already at the station, the approaching train will need to wait until the other train leaves
XXX Platform Closed XXX

## Slide 19
H.E. Holmes station

## Slide 20
Split platform at H.E. Holmes creates similar issues, prefer only one train there at a time

## Slide 21
Split platform at H.E. Holmes creates similar issues, prefer only one train there at a time

## Slide 22
What about single tracking in the middle of the line?

## Slide 23
What about single tracking in the middle of the line?
XXXXX TRACK CLOSED XXXXX

## Slide 24
What about single tracking in the middle of the line?
XXXXX TRACK CLOSED XXXXX

## Slide 25
transit scheduling
Thank you!